## Slide 1: AgWG Ad Hoc CAST Issues
March 23, 2021

## Slide 2: CAST-21 Workplan (Working Draft) *Approved data and method changes need to be finalized through the WQGIT by Sept. 1, 2021*
KEY ACTION | STATUS
Task 1: Updates to data & methods that typically occur every 2 years. | On-going May AgWG update: on-going ag data collecting projects
Task 2: Investigate alternative forecasting methods for ag land uses & animals | Nov 19 AgWG: CBPO presentation on 4 methods of forecasting Feb AgWG; March decision
Task 3: Investigate 2012-2017 Ag Census change for fallow/idle acres | AgWG Sept 17; NASS consulted; no new information; No further action; See Jan AgWG decision
Task 4: Investigate use of latest landcover & LiDAR imagery to better define changes in total ag (& other land use) acres | Oct AgWG; Jan AgWG; Feb AgWG; Apr AgWG; decision pending updated landcover & LiDAR imagery for 14 prototype counties May AgWG
Task 5: Investigate alternatives for double-crop acre estimates | Oct 15 AgWG; NASS consulted- no new information; No further action; no recommended change to methodology; May for decision (associated with Task 4 change to ag acre calculations)
Task 6: Consider supplemental NM for soybeans | In process Dec Ad Hoc; Jan Ad Hoc; Mar Ad Hoc; Apr-May AgWG
Task 7: QA/QC’d historic & current layer pop. data for Hillandale Farms (PA) | In process Feb Ad Hoc- general discussion; May AgWG
Task 8: Build-in Verification Ad Hoc Team products | In process
Questions/Comments?
https://www.chesapeakebay.net/channel_files/41834/cast21workplan_022221.pdf
Reminder - CAST 21 Schedule:
Sept 1, 2021 - All data and methods approved
Nov 1, 2021 - CAST-21 Beta release
Jan 1, 2022 - Final CAST-21 release

## Slide 3: Task 3: Investigate 2012-2017 Ag Census change for fallow/idle acres
Please send any objections WITH suggested modifications to the language below to Loretta Collins (lcollins@chesapeakebay.net) and Gary Felton (gfelton@umd.edu) by COB Thursday, February 4th.
No objections received
Decision:
The AgWG reached consensus regarding CAST-21 Workplan Task 3: Investigate 2012-2017 Ag Census change for fallow/idle acres, recognizing that the 5-year census indicates a significant increase in fallow & idle acres within some counties in the Chesapeake Bay watershed.
The AgWG acknowledges that investigation has not provided evidence to indicate that the 2017 Ag Census data is or is not reflective of on-the-ground change, therefore cannot recommend adjustment to CAST-21 model inputs at this time.
The AgWG has exhausted its available resources to investigate this issue, but this decision does not preclude interested parties from pursuing further lines of inquiry and bringing information back to the workgroup for review.

## Slide 4: Task 2: Investigate alternative forecasting methods for ag land uses & animals
Decision:
The AgWG approved a path forward regarding CAST-21 Workplan Task 2: Investigate alternatives to the current methods for forecasting agricultural land uses and animals and propose options for partnership consideration.
The AgWG achieved consensus to continue using the current projection method (Double Exponential Smoothing: Alpha = 0.8).

## Slide 5: PA Full Comments
We have met internally and reviewed the limited information provided by the PA Soybean Board which indicates that nutrients are being applied to full season soybeans in advance of planting. In this way, the model’s assumption of applied nutrients to these fields is conceptually correct.
The establishment of load without a means to reduce that load through control and uptake is a disconnection between the model assumptions and the interpretation of the EPR, which does not allow the application of Supplemental NM BMPs to these acres. Aside from the generally accepted N-fixation rate reduction with nutrient application (which cannot be answered at this time), we believe that the use of the Supplemental NM practices will have some beneficial effect that should be reflected in the model.
We could look at the specifics of Placement, Timing, and Rate relative to Soybeans in this EPR context, but we also think it would be helpful to have a CAST run that could look at what the overall effect of allowing one or all of these Supplemental Practices would produce in EOS loads. Having an understanding of what the effect would be on EOS loads has at times been very helpful in getting our workgroups closer to being able to tolerate a compromise decision when the science has not been fully developed. Having Olivia or Jess look at what this change might look like for No Action, Core only, and Core with each Supplemental (at say 5% implementation) in a county such as York might help the group consider options beyond the binary choices being discussed currently.
We could also look at varied rates of implementation for the scenario (5 to 50% ?). We would also want to confirm that these acres have been appropriately excluded from the E3 scenario and how the current interpretation of the EPR may be having unintended consequences with loads and targets. Having assistance from Olivia would be helpful in developing these scenarios and add an element of impartiality that the group will appreciate.
I personally think the Placement credit should be allowed without reservation, although I could understand the need to more thoroughly review and discuss the Rate and Timing practices and having EOS load change information could help the group’s decision. –Ted T.

## Slide 6: ACTION: PA will work on gathering information to better understand what real-world soybean management looks like. Other jurisdictions are encouraged to do the same.
Reviewed the limited information provided by the PA Soybean Board
Indicates that nutrients are being applied to full season soybeans in advance of planting.
In this way, the model’s assumption of applied nutrients to these fields is conceptually correct.

## Slide 7: PA Concern
Establishment of load without a means to reduce that load through control & uptake is a disconnection between the model assumptions and the interpretation of the Expert Panel Report (does not allow the application of Supplemental N NM BMPs on full-season soybeans)
Aside from the generally accepted N-fixation rate reduction with nutrient application (which cannot be answered at this time)*, we believe that the use of the Supplemental NM practices will have some beneficial effect that should be reflected in the model.
*attempt to answer that today

## Slide 8: PA Request
Look at the specifics of Placement, Timing, and Rate relative to Soybeans in Expert Panel Report context
CAST run that could look at what the overall effect of allowing one or all of these Supplemental Practices would produce in EOS loads: Understanding what the effect would be on EOS loads has at times been very helpful in getting our workgroups closer to being able to tolerate a compromise decision when the science has not been fully developed.
Look at what this change might look like for No Action, Core only, and Core with each Supplemental (at say 5% implementation) in a county such as York might help the group consider options beyond the binary choices being discussed currently. Varied rates of implementation for the scenario (5 to 50% ?) Want to confirm that these acres have been appropriately excluded from the E3 scenario and how the current interpretation of the Expert Panel Report may be having unintended consequences with loads and targets.

## Slide 9: Initial Response (to PA request)
Understanding the potential reduction from Supplemental N NM application to soybeans is easier than running scenarios in CAST
“The supplemental N NM BMPs are to address the N applications to soybeans. Soybeans fix nitrogen and most of the load increase from the increase in soybeans and decrease in double cropped was from the fixation. This has nothing to do with any BMP. Using NM Placement, Timing, and Rate on soybeans will reduce the small application where it exists, but not stop the fixation. The efficiencies applied to the other land uses for those three BMPs are below. The higher percentages are all for crops eligible for manure.” –Olivia D
Since the Supplemental BMPs are applied the edge-of-stream load (rather than Crop Application Goal), you can reduce known full-season soybean N load by the percent efficiency.
If the load from soybean acres is 1,000 lbs., then a reduction at 5% would mean 950 lbs. for the TN load.
NM BMP | N Efficiency (pct) | P Efficiency (pct)
Placement | 3 | 10 or 20
Rate | 5 or 15 | 5 or 10
Timing | 5 or 10 | 1 or 20

## Slide 10: ACTION: Clarify with CBPO how the simulation of how N assumptions are handled in the model (e.g. reduction of N fixation in the model with applied N).

## Slide 11: Crop Application Goal on Major Crops lbs of N/Year = State-Supplied lbs of N/Application Goal Yield Unit/Year X Yield/Year X 1.1*
Crop | DoubleCrop | Nutrient | Yield Unit | DE_1 | MD_1 | NY_1 | PA_1 | VA_1 | WV_1
Alfalfa Hay Harvested Area | N | TN | dry tons | 1 | 1 | 1 | 1 | 1 | 1
Alfalfa Hay Harvested Area | N | TP | dry tons | 5 | 5 | 5 | 6 | 5 | 5
Corn for Grain Harvested Area | N | TN | bushels | 0.92 | 0.92 | 0.92 | 0.92 | 0.92 | 0.92
Corn for Grain Harvested Area | N | TP | bushels | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
Corn for Grain Harvested Area | Y | TN | bushels | 0.92 | 0.92 | 0.92 | 0.92 | 0.92 | 0.92
Corn for Grain Harvested Area | Y | TP | bushels | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
Wheat for Grain Harvested Area | N | TP | bushels | 0.31 | 0.31 | 0.31 | 0.31 | 0.31 | 0.31
Wheat for Grain Harvested Area | N | TN | bushels | 1.25 | 1.25 | 1 | 1 | 1.25 | 1.25
Wheat for Grain Harvested Area | Y | TP | bushels | 0.465 | 0.465 | 0.465 | 0.465 | 0.465 | 0.465
Wheat for Grain Harvested Area | Y | TN | bushels | 1.25 | 1.25 | 1 | 1 | 1.25 | 1.25
Pastureland and rangeland other than cropland and woodland pastured Area | N | TN | acres | 15 | 15 | 15 | 15 | 15 | 15
Pastureland and rangeland other than cropland and woodland pastured Area | N | TP | acres | 4 | 4 | 4 | 4 | 4 | 4
Soybeans for beans Harvested Area | N | TN | bushels | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
Soybeans for beans Harvested Area | N | TP | bushels | 0.33 | 0.33 | 0.33 | 0.33 | 0.33 | 0.33
Soybeans for beans Harvested Area | Y | TN | bushels | 0 | 0 | 0 | 0 | 0 | 0
Soybeans for beans Harvested Area | Y | TP | bushels | 0 | 0 | 0 | 0 | 0 | 0
Data provided by states after consultation with nutrient management program staff.
Chesapeake Bay Program Phase 6 Beta 3 Watershed Model Webinar
July 11, 2016
CRITICAL CONTEXT:
“Crop Application Goal” assumes Core NM is in place
Full Season Beans receive
0.12 lb N/bu
&
0.33 lb P/bu
Double Crop Beans
(application is on sm gr)
0 lb N/bu
&
0 lb P/bu
NM on full season beans is controlling/managing for phosphorus!
*AMS elected to multiply yearly yield by 1.1 assuming farmers are optimistic, and average yields are often under-estimated.
Crop Application Goal

## Slide 12: Application Goal Multipliers (CORE)
Land Use | Non NM N Multiplier | NM N Multiplier | Non NM P Multiplier | NM P Multiplier
Full Season Soybeans | 1.2 | 1.0 | 1.5 | 1.0
Grain with Manure | 1.3 | 1.0 | 3 | 1.0
Grain without Manure | 1.2 | 1.0 | 1.5 | 1.0
Legume Hay | 1.2 | 1.0 | 1 | 1.0
Silage with Manure | 1.4 | 1.0 | 3 | 1.0
Silage without Manure | 1.2 | 1.0 | 1.5 | 1.0
Small Grains and Grains | 1.2 | 1.0 | 1.5 | 1.0
Small Grains and Soybeans | 1.2 | 1.0 | 1.5 | 1.0
Specialty Crop High | 1.3 | 1.0 | 2 | 1.0
Specialty Crop Low | 1.2 | 1.0 | 2 | 1.0
Other Agronomic Crops | 1.1 | 1.0 | 1.5 | 1.0
Other Hay | 1 | 1.0 | 1 | 1.0
Pasture | 1 | 1.0 | 1 | 1.0
Data provided by Phase 6.0 Nutrient Management Expert Panel
Full Season Soybeans:
40 bu/ac @ 100 ac
Core NM:
40 bu/ac x 0.12 lbs N/bu x 1.0 x 100 ac =
480 lbs N applied
40 bu/ac x 0.33 lbs P/bu x 1.0 x 100 ac =
1,320 lbs P applied
Non NM:
40 bu/ac x 0.12 lbs N/ac x 1.2 x 100 ac =
570 lbs N applied
40 bu/ac x 0.33 lbs P/bu x 1.5 x 100 ac =
1,980 lbs P applied
CRITICAL CONCEPT:
Multipliers are applied to Crop Application Goal

## Slide 13
https://cast.chesapeakebay.net/FileBrowser/GetFile?fileName=P6ModelDocumentation%2F3TerrestrialInputs.pdf

## Slide 14: Agricultural Modeling Subcommittee (AMS) June 13, 2016: Discussion on Application Rates for Soybeans
    Keppler: I know we had a conversation about manure on soybeans, and I don’t think the land use currently allows for that.
    Dubin: The land use that was developed by the subcommittee didn’t include the manure application on soybeans.
    Keppler: So this table reflects potential applications on soybeans, so there may be some disconnect, and this would be commercial fertilizer?
    Johnston: So do we move forward with this approach on the table and resurrect that group to describe that soybeans do receive manure, or do we move forward with soybeans not receiving manure, and Chris would revise that 0.17 value. Regardless of the LGU recommendations, I know soybeans get manure.
    Long: Soybeans get manure, biosolids, and N from commercial fertilizer. One consideration though is that the P getting applied through the commercial fertilizer is DAP.
    Coale: This is a tough one, but this might have to be handled with an asterisk and a footnote somehow.
    Keppler: If the intent is to make the model as close to reality as possible, then I think we should have some type of mechanism to allow fertilizer and manure on soybeans.
    Coale: That’s fine, but then those acres would not qualify for NM on soybeans.
    Johnston: That’s even more difficult, because we don’t have it set up to distinguish soybeans as those that receive and don’t receive manure.
    Meisinger: But you do have a separation of NM vs. non-NM soybeans, so you could add an incidental commercial fertilizer application to represent DAP on the non-NM soybean acres.

## Slide 15: Agricultural Modeling Subcommittee (AMS) June 13, 2016: Discussion on Application Rates for Soybeans
  Johnston: So that question might have to be posted to the AgWG and the NMP - What to do with soybeans acre they received NM plans from that are receiving manure? But is everyone comfortable with adjusting soybean N to represent incidental DAP applications, and allowing the NMP to set higher application on non-NM acres that would include manure?
    Group felt comfortable moving forward with that decision.
    DECISION: The AMS agreed to set soybean application rates for Nitrogen to reflect incidental inorganic application of diammonium phosphate. This will allow the NMP to increase the non-NM rate to account for acres that might receive manure.
  Johnston: I would recommend we start with 0.33 and do the equation to convert that to DAP. Then this table would represent the NM condition for soybeans, and the NMP could tell us what the multiplier is for that, considering manure and inorganic fertilizer.
    Brosch: I wouldn’t recommend using DAP.
    Long: I would argue that DAP is more the norm than the exception.
    Johnston: So can we use that as the justification? The recommendation was to back up from 0.33 to account for DAP.
    Keppler: If manure’s being taken out of the equation, I’m happy with the resulting recommendation. We don’t have to worry about breaking out manure v. non-manure soybean acres; I just want this to reflect the commercial application.
    PA stated they would be comfortable backing down the 0.17 to reflect that ratio as well.
    AMS reached consensus; Chris Brosch will revise the table accordingly.
    DECISION: The AMS agreed to eliminate the TP and TN application rates for double-cropped soybeans, assuming it will go into small grains (wheat, oats, barley).
https://www.chesapeakebay.net/channel_files/25175/ams-agwg_decisions_on_p6_model_2015-2017_2.pdf
Crop Application Goal Reduced to .12 to reflect DAP ratio

## Slide 16: Soybean Crop Application Goal
Full Season Soybeans
0.12 lbs N/bu (~5.7 lbs N/ac)
CBW Average: (~3.58 lb/N ac)
UME, Penn State, VT recommend zero N application
Double Cropped Soybeans
Zero N applications
UME, Penn State, VT recommend zero N application
Assumption: “Nitrogen application is not recommended for soybean production, however, use of commercially available fertilizer formulations may result in application of up to 50 lb N / acre when fertilizer formulation and application rate is determined by crop P2O5, K2O, S, or other nutrient needs. Organic waste nitrogen application to full-season soybean is not recommended because it is an agronomically inefficient use of applied nutrients. Organic wastes should only be applied to small grain - double-crop soybean rotations at rates and timings to supply the recommended nitrogen rate to the small grain crop.” – UME SFM-1

## Slide 17: NM Supplemental Percent Reductions (Only after Core NM is applied)
Data provided by Phase 6.0 Nutrient Management Expert Panel
CRITICAL CONCEPT:
Supplemental NM is applied to Edge of Stream Delivery
NM BMP | N Efficiency (pct) | P Efficiency (pct)
Placement | 3 or 5 | 10 or 20
Rate | 5 or 15 | 5 or 10
Timing | 5 or 10 | 1 or 20

## Slide 18
https://cast.chesapeakebay.net/FileBrowser/GetFile?fileName=P6ModelDocumentation%2F3TerrestrialInputs.pdf

## Slide 19
https://cast.chesapeakebay.net/FileBrowser/GetFile?fileName=P6ModelDocumentation%2F3TerrestrialInputs.pdf

## Slide 20: ACTION: Clarify with CBPO how the simulation of how N assumptions are handled in the model (e.g. reduction of N fixation in the model with applied N).
CAST Assumptions & Mechanics
  Increase in Soil N or Applied N will decrease N fixation
  45 lbs./ac Soil N available
  ~77% of uptake from N fixation
    If zero N is applied
    w/ N application fixation fraction will decrease
  5.31 lbs. N fixation /bu
  3.54 lbs. N removal/bu
% Fixation |  |  | Soil N + appl. N (CAG) |  |  | Soil N2
77.3 | 98.61 | 0.5107 | 45 | No Applied N | 0.000829 | 2025
75.2 | 98.61 | 0.5107 | 49.8 | 40 bu/ac | 0.000829 | 2480.04
75.0 | 98.61 | 0.5107 | 50.4 | 45 bu /ac | 0.000829 | 2540.16
74.7 | 98.61 | 0.5107 | 51 | 50 bu/ac | 0.000829 | 2601
74.2 | 98.61 | 0.5107 | 52.2 | 60 bu/ac | 0.000829 | 2724.84

## Slide 21: Assume 50 bu/ac
% Fixation |  |  | Soil N + appl. N (CAG) #/ac | Yield |  | Soil N2
74.72105 | 98.61 | 0.5107 | 51 | 50 bu/ac | 0.000829 | 2601
74.7 % N fix. * 50 bu/ac *3.54lbs. N crop removal/bu = 132 lbs. N fix uptake/ac
132 lbs. N fix/ac * 1.5 = 198 lbs. N fix total /ac
198 lbs. N fix total/ac + 45 lbs. Soil N/ac + 6 lbs. N applied/ac = 249lbs. total N/ac
249 lbs. total N/ac – 177 lbs. N crop removal /ac = 72.38 lbs. N/ac available for loss
Crop Removal Multiplier (calculates crop uptake)

## Slide 22: 72.38 lbs. N/ac available for loss
Potential N loss | N Efficiency | lbs. N loss reduction | BMP
72.38 | 0.05 | 3.619219 | Placement
72.38 | 0.05 | 3.619219 | Timing
72.38 | 0.05 | 3.619219 | Rate
 | Total | 10.85766 | 
Crop Application Goal for N @ 50 bu/ac is 6 lbs. N/ac
Applied N (CAG) is ~ 2% of total system N (249 lbs. /ac= fixation/soil/applied)
72.38 lbs. N is ~30% of 249 lbs.
30% of 6 lbs. N = ~2 lbs. N/ac
One Supplemental BMP @ 5% efficiency would remove more N than was applied (assuming all N sources behave proportionally- CAST lumps them all together at the front end)

## Slide 23: Straw Poll- Where do you lean now?
Current Ask: Change Nutrient Management Expert Panel Recommendations apply non-zero reduction efficiency value for Supplemental Nitrogen Nutrient Management BMP on full-season soybean load source (Rate, Timing, and/or Placement)
DE- on the fence
  recommend small amount on 60-70 bu soybeans (high-yield)
    <30 lbs N
MD- leaning “no” recommend small amount on 60-70 bu soybeans (high-yield)
  allow manure application (regulatory)
NY- on the fence (confer with NY team)
PA- yes based on 4R practices
  EP assumes no manure application, but is applied
  Full-season soybean in E3 scenario? Expected that these acres have supplemental NM?
    Are the planning targets based on acres related expected on soybeans?
    E3 based on 2010. That has not changed. Fewer soybeans expected in 2010. E3 may be working to PA’s advantage.
      Soybeans included in crop/hay group-100% NM implementation
VA- leaning to no
  Input issue, rather then BMP issue
  Manure application under regulations- but not for nutrient management
WV- ?
Ken Staver (at-large)- where manure is applied want to encourage minimizing losses
  What does manure application on soybeans, what does it look like?
    What would supplemental BMP look like?

## Slide 24: Next Steps?
  Short-Term
Actionable/decision item for the AgWG Apr-May-June?
  Sept 1 Deadline for CAST-21 Workplan resolution
  BMP protocol a concern
  Clarification of E3 concern for communication to CBP stakeholders
  MD/DE research manure by April Ad Hoc to firm up position Supplemental N BMP (soybeans)
  NY- Emily confer w/ Cassie & Greg
  WV?
  VA – ask about what else there is to find
Long-Term
Phase 7 Review of Ag Loading Rates/Ratios
  Identification & consideration of new literature/sources
    N fixation
    Soybean (& other crop management)

## Slide 25: What is Driving N Load Concerns?
Agricultural Loading Rates?
Ag Census (i.e., Source Of Crop Data) ?
NM BMP Recommendations?
Changing an Approved Expert Panel Recommendation Must Follow Science (BMP Protocol)
Protocol for the Development, Review, and Approval of Loading and Effectiveness Estimates for Nutrient and Sediment Controls in the Chesapeake Bay Watershed Model
No consensus in Ad Hoc yet…

## Slide 26: Agricultural Loading Rates
Agricultural Loading Rates
Based on Available Literature & Best Professional Judgement
“N losses from soybeans are only somewhat lower than corn, because N fixation inputs (which are poorly characterized) are apparently substituting for fertilizer inputs.” (p.11 )
Ag Loading Rate Review Steering Committee: Agricultural Loading Rates

## Slide 27: Census of Agriculture
Concern Regarding Accuracy of Ag Census Crop Acres
Spatially Distributed Land Use from the Land Cover/Land Use Data Team Starting With the CAST-21 Could Mitigate Concern
Method of Modeling Double-Crop Soybeans Approved by CBP Partnership
Determined Sound by USDA-NASS
CAST-21 Workplan
TASK 6

## Slide 28: NM Expert Panel Recommendations Land Use: Full-Season Soybeans
NM on Soybeans Controls for P (not N)
Land Grant Universities Do Not Recommend N Application (Via Fertilizer or Manure)
Core NM BMP  N & P
Applies to Crop Application Goal (What is Applied/Distributed to Crop)
  Small CAG for N on soybeans allows for appropriate distribution of nutrients across land uses (see reference slides)
Supplemental NM BMPs (Rate, Timing, Placement) P only
Applies to Soybean Edge-of-Field Total N Load
  TN Load is Primarily Residual N From Fixation
  Applied (CAG) N is Tiny Fraction of TN Load
Rate: Excess N Reduced is Still Excess N Subject to Loss…
Timing & Placement of Excess N Irrelevant (Still Subject to Loss)

## Slide 29
Animal Data
Animal Populations: explore other estimating options (MD/NY; Task 1)
Crop Production/Acres
Crop Production Acres: improve annual estimates (MD; Task 1)
Nutrient Applications/Assumptions
Fertilizer Sales and Use Data (MD; Task 1)
BMP Tracking & Reporting
Dairy Precision Feeding (PA)
BMP Effectiveness/Modeling
Winter Crop (NY/PA)
Manure Transport / Manure Treatment Technologies (PA)
Target Date June 2021 for Report Back to the AgWG
Forthcoming Discussions
Future Discussions with Modeling Team
MD Working w/ State Chemist
CBPO- NASS annual dairy surveys
AgWG May Updates

## Slide 30: Improving Ag Data? (TASK 1)
CRITICAL CONCEPT:
To maintain integrity of CBWM there are two options for new data sets:
Provide data all the way back through 1985.
OR
Use the trend in new data sets for the years available.
CBWM= Chesapeake Bay Watershed Model
Crop Acreage Data
Alternative methods to account for fitting Ag Census data to CBP needs?
  Adjusting methods for estimating crop acres (e.g. double crops)
Alternative/supplemental data sets
  Other data sets at the state or federal level?
Animal Population Data
Additional NASS Annual Survey Data may be available to inform population trends between census years (incorporated every two years)
  Dairy, Beef Cattle, Layers, Swine…
Direct from industry data can inform animal population trends between census years.
  Requires careful cooperation
  Legal, privacy assurances
Other Data Issues (new data incorporation every 2 years)
Soil P data
  Gary Shenk Sept 2018 presentation to AgWG on data set incorporated into the CBWM
  Additional soil P data is welcome and encouraged (NY & WV have made inquiries)
Manure Nutrient Concentration Data
  Changes in management may result in changes in nutrient concentrations
  Additional manure concentration data is welcome and encouraged
  Fertilizer Data
  More accurate allocation of fertilizer within the CBW?
    Jurisdictions working with state chemists
Crop Application Goal
Manure Generated
4. Define Inorganic Fertilizer Available to Crops

## Slide 31: Prioritizing Concerns (post CAST-21)
AgWG Home Page https://www.chesapeakebay.net/who/group/agriculture_workgroup
Ad Hoc November Recommendation: Create a tracking mechanism for jurisdictions’ wish list for 2-year CAST updates & the next model phase.

## Slide 33
April AgWG CAST Concerns Ad Hoc:
  Clarification “Winter Crop” BMP Ask
  NM on Soybeans
April AgWG
  Discussion Landcover/ LiDAR Data (Task 4)
  Detailed update NM on Soybeans (Task 6)
May AgWG
  Decision Landcover/ LiDAR Data (Task 4)
  Decision Double Crop Methods (Task 5)
  NM on Soybeans (Task 6)
  Hillandale Data (Task 7)
June
  Update from Dairy Precision Feeding Group

## Slide 34: AgWG CAST Concerns Ad Hoc Jurisdictional reps reviewing submitted concerns Monthly updates to the AgWG
Feb Ad Hoc
Feb AgWG
Mar Ad Hoc
Apr AgWG
Apr Ad Hoc
Apr AgWG
Ad Hoc November Recommendation: Create a tracking mechanism for jurisdictions’ wish list for 2-year CAST updates & the next model phase.

## Slide 36
BMP Concern | CBP BMP Effectiveness Source | Next Steps
Dairy Precision Feeding (PA) | Definitions and reductions approved by the WQGIT in 2009 | PA Action Team
Rotational/Prescribed Grazing (PA) | Definitions and benefits were reviewed and approved by the Agriculture Workgroup and WQGIT in 2010 | RESOLVED
Heavy Use Area Protection- NRCS 561 (PA) | Loafing Lot Management definitions and reductions approved by the Chesapeake Bay Program’s Nutrient Subcommittee in 2003. | ?
Nutrient Management on Pasture (NY/PA) | Nutrient Management Practices for use in the Phase 6.0 Chesapeake Bay Program Watershed Model (2016) | RESOLVED
Commodity Cover Crops (NY/PA) | Cover Crops Practices for use in Phase 6 of the Chesapeake Bay Watershed Model (2016) | EP Chair discussion with AgWG (Dec 2020)
Manure Transport / Manure Treatment Technologies (PA) | Manure Treatment Technologies: Recommendations from the Manure Treatment Technologies Expert Panel to the CBP’s WQGIT to define Manure Treatment Technologies as a Best Management Practice (2016) Manure Transport: definition and benefits have remained in use since review and approval by the CBP partnership’s source sector workgroups for tributary strategy development. | Work with MWG
Protocol for the Development, Review, and Approval of Loading and Effectiveness Estimates for Nutrient and Sediment Controls in the Chesapeake Bay Watershed Model

## Slide 37
1.Define Crop Application Goal
A
Crop Application Goal/Yield Unit
B Yields/Acre
C
Acres
Crop Application Goal
2. Define Manure Available to Crops
Manure Generated
Direct Deposition on Pasture
Direct Deposition to Riparian Pasture Areas
Deposited within Barnyard
Storage and Handling Loss
Stored Manure
Manure Transport
Feed Additive BMPs
Volatilization
Available for Application
Barnyard BMPs
Ammonia Reduction BMPs
Available for Transport
Mineralization
3. Spread Manure to Crops
4. Define Inorganic Fertilizer Available to Crops
5. Spread Fertilizer to Crops
Ag Census or
NASS Annual Surveys
(Animal populations dictate manure load estimates)
A AMS
B NASS Annual Survey
C Ag Census
AAPFCO Fertilizer Sales Data
Allocation of Ag Nutrients in the Watershed Model
AMS= Agricultural Modeling Subcommittee

## Slide 38: Comments on CAST-19: Soybean nitrogen application (p.2)
With the increase in full-season soybeans and decrease in double cropped soybeans in CAST-19, the N application rates were examined. Chris Brosch-DDA, Jill Whitcomb-PA-DEP; James Martin-VA-DEQ

## Slide 39: Comments on CAST-19: Soybean nitrogen applicationResponse (p.3)
N applications on soybeans depend on whether the soybeans are full season or double cropped.
Double-cropped receive 0 N applications.
Full season have a N crop need of 0.12 lb./bu (5.70 lbs./ac)
  watershed-wide avg
    2.23 inorganic lbs./acre applied
    1.35 organic lbs./acre applied
The University of Maryland, Penn State, and Virginia Tech nutrient management guidelines recommend zero N on full-season or double-cropped soybeans.

## Slide 40: Comments on CAST-19: Soybean nitrogen application_Resolution (p.3)
A comparative analysis of changing full-season soybeans to corn and the resulting nitrogen loads was provided to PA-DEP.
The soybean N application and N fixation assumed for Lancaster County and the average in the rest of PA’s watershed were provided to Jill Whitcomb, PA-DEP.
The CBP will provide to Jill Whitcomb, PA-DEP, and other states the peer reviewed research and other sources that document nutrient runoff/leaching rates from legumes, and how it is applied in the modeling tools (e.g., is it a constant throughout the year or is there a difference in seasonality, is there a difference depending on what crop preceded/followed, etc.) by the May 25, 2020 WQGIT.
The AgWG will be asked to consider establishing a group to evaluate nutrient management BMPs for nitrogen on full season soybeans. [see Workplan Task 6]

## Slide 41: N Application on Soybeans
From Water Quality GIT presentation to Management Board 7/9/20

## Slide 42: Concern:
Full Season (under Core NM):
Assume 40 bu/ac @ 100 ac
40 bu/ac x 0.12 lbs N/bu x 1.0 x 100 ac =
480 lbs N applied
Double-Crop
Assume 25 bu/ac @ 100 ac
25 bu/ac x 0 lbs N/bu x 1.0 x 100 ac
0 lbs N applied (on beans)
N applied to sm grain
Model Assumption
CRITICAL CONCEPT:
N load attributed to soybean acres includes estimated leaching/runoff of residual N based on scientific literature review.
Agricultural Loading Rates
Ag Loading Rate Review Steering Committee
Nutrient management on full-season soybeans?
YES: “core NM”
  NO: “supplemental NM” for N rate, placement & timing
    Why? NM on soybeans is controlling for P…
Given the same acreage…
A shift from double-crop to full-season soybeans will result in an increase in attributed N load.

## Slide 43: Source for distribution of statewide populations can change.
  Example: Pennsylvania provides fraction of cattle in every county for the year 2019, and these fractions are used to distribute TOTAL statewide cattle populations from the Census of Agriculture.
Census
100 Cattle
County A
35%
Outside Watershed
15%
County C
50%
County B
0%
PA Data
(75 Cattle)
100 Cattle
County A
25%
Outside Watershed
25%
County C
40%
County B
10%
Source of TOTAL statewide populations will not change for Phase 6 Watershed Model.
CRITICAL CONCEPT