## Slide 1: Interpolator Grid: Proposed thinning 5 segments
BORG meeting
Nov. 17, 2025
Rebecca Murphy (UMCES/CBP), Jon Harcum (Tetra Tech),
Elgin Perry (statistics consultant)

## Slide 2: Background
For criteria assessment purposes, DO data is interpolated to a grid that fills the volume of each segment.
A spatial grid exists that has been used for the 3-D interpolator:
  Vertical resolution = 1m layers
  Horizontal resolution = cells ranging from 50m x 50m to 1km x 1km
For consistency, we intended to use that same grid for the 4-D spatial output.
Cell size | Number of segments | Area (km2)
50 m | 15 | 91
100 m | 15 | 265
250 m | 19 | 497
500 m | 26 | 2,467
1 km | 17 | 8,341

## Slide 3: Testing with 4D
One of our goals is usability on a standard 32-GB laptop for ease of transfer to you.
Testing the 4-D simulation runs in every segment indicated five segments that either didn’t run (or inconsistently ran) on a laptop. They all ran on a workstation with more RAM.
When the grid was thinned for each of these, they ran on the laptop.
 | Run time [min] | 
Segment | Current Grid (128 GB workstation) | ½ Thinning (32 GB laptop)
CHOTF | 6.85 | 2.41
MPNTF | 12.81 | 5.59
NANOH | 28.32 | 3.21
PMKTF | 19.61 | 6.67
HNGMN | 24.98 | 8.70

## Slide 4
MPNTF: Mattaponi tidal fresh
Centroids with a 50m grid
100m grid

## Slide 5
HNGMH: Honga mesohaline
Centroids with a
100m grid
250m grid*
*Note that numeric thinning tests were performed on 200m grid

## Slide 6: Impact: DO analysis
Interpolation results were compared between the original grid and thinned grid.
We superimposed empirical distribution functions (EDFs) of 4-D interpolator simulation results for the two grid resolutions.
12 months of comparisons were done for 2 of the segments.
There is very little difference in the simulation results due to thinning.
This means that the thinner grids still represent the DO concentrations, bathymetry, and variability just as well as the dense grids.
Specific EDF results will change slightly due to these being generated with a draft version of the tool.
Blue=full
Green=
thinned
*
*EDF is from DRAFT 4-D simulation results and exact values and range of simulations will likely change.

## Slide 7: Impact: DO analysis
Blue=full
Green=
thinned
*EDFs are from DRAFT 4-D simulation results and exact values and range of simulations will likely change.
*
*

## Slide 8: Impact: DO analysis
Blue=full
Green=
thinned
*EDFs are from DRAFT 4-D simulation results and exact values and range of simulations will likely change.
*
*

## Slide 9: Summary
The proposed adjustments are only to the horizontal grid resolution in 5 segments out of 92. And there are no adjustments proposed to boundaries of segments.
We saw no impact of these grid changes on the shape of the EDF graphs for the DO interpolation results in two of the segments tested.
Thus, it is not expected that this grid thinning will result in any different conclusions regarding criteria assessment.
These grid resolution edits would, however, have a large impact on a user’s feasibility of running the 4-D tool in terms of computing power needed and run time.