## Slide 1: Timber harvest reporting, mapping and modeling in Phase 7
April THTF meeting

## Slide 2: Current process for modeling timber harvest acreages
Some states reports harvested forest acreage to CBP at county scale
  Reported harvested forest acres are proportionately allocated to sub-county modeling units (land-river segments, LR Segs) by the CBP based on the relative amount of “true forest” within each unit
States that don’t report harvested forest acreage have the default rate (currently 1.5%) applied proportionately based on the distribution of true forest across LR Segs
USGS maps clearcuts every 4-5 years (and interpolates for intervening years)
Both mapped and reported/default acres are subtracted from “true forest”
  Clearcuts are getting double-counted! This is a particular issue for states with significant amounts of clearcuts
Notes: This presentation will help walk us through some options for improving the way we count timber harvest acreages in the model and how we model their spatial distribution. This is an issue brought up in previous meetings about needing to 1) consider how we allocate reported harvest acres at county scales to catchments based on the LULC and 2) reconcile the reported and mapped harvest acres.
- For both reported forest harvests and default harvested forest, these acres get pulled from “true forest” as harvested forest
Mapped harvests get modeled as mixed open, but again are subtracted from “true forest”
This issue with clearcuts is one issue we want to address in Phase 7

## Slide 3: Proposed process for Phase 7
States continue to report harvest data at the county scale
Mapped clearcut data gets aggregated up to the county scale, and averaged into an annual mapped harvest rate over the 4-5 years of land use data
Annualized mapped clearcut acreages are subtracted from the total reported harvest acreage (or default harvest acreage) at the county scale
Mapped clearcuts are distributed back to their original catchments
Distribute unmapped portion of harvested forest acreage across NHD catchments within each county based on:
  Option A: amount of true forest in each catchment
  Option B: relative amounf of “harvestable” forest in each catchment
  Not all true forest is harvestable or likely to be harvested. Forests in rural areas with large patch and parcel sizes may be the most likely candidates for future harvest
Notes: We have developed an approach that would get around this double-counting issue without requiring the states to change their reporting methods to distinguish clearcuts from other forms of harvest. Want to get input.

## Slide 4: Issues to resolve
How to define “harvestable” forest?
How to consistently back-cast forest harvest acres through the Phase 7 model calibration period (1985-2022)
  For states that are reporting- how can we use the reporting data to estimate harvest rates in years before reporting began?
    Reporting years:
      MD: 2002-2023
      VA: 1993-2023
      WV: 1985-2023
    Should we use the average reported harvest numbers over the reporting period?
  For states using the default- would there be a reason to use a different/varying harvest rate over the calibration period (e.g., periods of high harvest vs low harvest)?