## Slide 1: Lower Susquehanna River Dam Sediment and Solutions
Conowingo Relicensing; LSRWA; MD County Resistance; Solutions;
CAC Involvement
Thursday November 29. 2012

## Slide 2
Exelon and Conowingo Relicensing
Exelon Application states, “The cumulative impact of the Project to the system is to provide the last site of sediment storage along the Susquehanna River before sediment reaches Chesapeake Bay. This has benefited Chesapeake Bay by providing a means by which the quantity of fine-grained sediment and associated nutrients, sources of water quality impairment, reaching the Bay are reduced.”
Exelon Application states, “In summary, the impact of the Project on sediment, when added to other past, present, and reasonably foreseeable future actions, is beneficial or small. When the Project reaches steady state, these benefits will be reduced.”
LSR Response, “The model used by Exelon to determine there is no scouring, HEC-6, is not an appropriate model for this calculation, and Exelon’s consultants have been informed of this by USGS. ACE info and bathymetry from 1972 event, and others, indicate that large amounts of sediment are transported to the Chesapeake Bay by scouring and these events can have a major negative impact on the Chesapeake Bay.”

## Slide 3: CONOWINGO POND BATHYMETRIC SURVEY
  Sediment Task Force Meeting January 23, 2012 Marjorie L. Zeff, PhD., PG (URS) Gary Lemay (Gomez & Sullivan)
  USGS XC 19 and upstream are likely in dynamic equilibrium
    Some areas of deposition and scour, but generally balanced
  In the lower Pond (USGS XC 20 and below), deposition outweighed scour
    Average cross-section depths generally decreased by 1 foot to 3.5 feet
  Deposition occurred around banks/edges, scour in the main channel
  Conowingo Pond accumulated approximately 5,870 acre-ft of sediment between the 2008 survey (fall 2008) and 2011 survey (late October 2011)
  Net sediment deposition between the 2008 and 2011 surveys was 8.67 million tons, which translates to approximately 2.9 million tons of deposition per year
  For reference, historic deposition rates have ranged from 3.1 million tons/yr from 1929-1958, to 2.5 million tons/yr from 1958-1993, to 1.5 million tons/yr from 1996-2008 (Langland 2009)

## Slide 4: Lower Susquehanna River Watershed Assessment (Sediment Task Force)
Preliminary Model Runs by CBP show future impacts to Upper and Middle Chesapeake Bay due to loss of trapping capacity
This model was run at only 1/5th of actual expected sediment loading
Effects to Susquehanna Flats caused by pass-through of additional 286,000 tons: Chlorophyll up 3-5 ppm, DO down .5-1 ppm, Light Extinction Events Worsen Greatly, Loss of 7% of SAV

## Slide 5: Funk and Bolton TMDL Coalition
Due greatly to publicity regarding the effects of increased scouring events and loss of sediment trapping capacity, a Chestertown law firm has taken advantage of this information to promote anti-TMDL action
Allegany, Caroline, Carroll, Cecil, Dorchester, Frederick and Kent Counties
LSR is working with CBP and MDE to open communications with counties and set up presentations

## Slide 6: Solutions
Upstream BMP’s: Agriculture, Urban, Transportation, Forestry, Mining, Stream Stabilization, Sediment Trapping Structures, Riparian Buffers, Wetlands, Nutrient Trading
Bypassing: Bypass Systems, Modified Dam Operations, Sediment Pass-Through by Lowering Water Levels, Release Turbidity Density Currents (open lower gates), Off-Stream Reservoir, Tunnel Bypass
Increase or Recover Sediment Retention Volume: Dam Removal, Enlarge Storage, Sediment Fixing, Floating Islands, Dredging to Maintain Capacity, Complete Dredging, Hydraulic Dredging-Pressure Flushing (opening gates)
Innovative Reuse: Island Restoration, Soil Amendment for Agriculture, Soil Amendment for Mining, Lightweight Aggregate, Beach Renourishment, Landfill Cover

## Slide 7: Citizen Involvement and Engagement Opportunities
Conowingo Relicensing: REA - Environmental Assessment, Maryland State Environmental Certification – LSR can be a resource and representative for CAC
PA State and PA Dams: Advocate of state officials for responsibility of PA as a source, and of PA dams as sources
Funk and Bolton, Maryland Counties: Advocating/Discussing issues with local elected officials- local LTE’s from local citizens
Federal and State Funding of Solutions: As of today, no solution is known that is completely based on free-market profit. Some funding from for-profit entities and taxpayers may be necessary. The options of how this can occur appear to LSR to be through the Conowingo licensing process and federal and state legislation.