## Slide 1: Point Sources Progress Reporting
Management Board Conference Call
February 9, 2012

## Slide 2
Nutrient Reductions Progress Reporting
Annual Progress Report: The annual progress report should assess the success of the implementation efforts from the preceding year’s action plan.
Indicator: A valid indicator of progress must hold constant everything except the change that is being measured.
Issue: The point source progress measure is not measuring implementation progress, it is measuring the combined influence of progress and flow.
By not accounting for WWTP flow, an understanding of progress is confounded.

## Slide 3: 2010 Status Report Nutrient Loads Delivered to the Bay
Loads delivered to the Bay over past year
Influenced by precipitation.
The existing indicator should be retained as the primary indicator, and as an indicator of status.
Chart Source: EPA Chesapeake Bay Program

## Slide 4
Current Progress Reporting Approach
Inconsistent approach for point and nonpoint source indicators.
EPA reports non-point source nutrient reductions progress based on the watershed model that uses a 10 year hydrologic averaging period that is applied to the most recent implementation efforts
This approach reduces the influence of annual variation in flow and provides a better indication of “on the ground” progress.

## Slide 5
Current Progress Reporting Approach Point Sources
EPA reports point source progress based on most recent year information from Discharge Monitoring Reports (DMRs).
Flows vary with precipitation due to infiltration and inflow (I & I) into the collection system
Because of this, the current progress indicator is confounded by flow changes caused by precipitation that varies annually, thus masking reductions (or increases) in effluent concentrations.
This is not an accurate progress report for decision makers or the public.

## Slide 6: Point Sources Progress Reporting
Issues/Concerns:
  How to make PS and NPS comparable in Progress Scenarios, Milestones, Bay Barometer.
  The influence of annual variation in precipitation or any other confounding factor must be removed from both.
  Follow up with 2009 Executive Council decision to report “Practices in Place.”

## Slide 7: Point Sources Progress Reporting
Actions Requested:
  Provide feedback on proposed supplemental indicators for PS progress reports (e.g., nutrients concentrations, # of upgraded facilities)
  Provide feedback on methodology to estimate PS loads for Progress reports; decide on flow averaging period
  Prepare to present issue to PSC if necessary.

## Slide 8
Example of Flow used in Current Progress Reporting
Are we comparing Apples and Oranges?
NPS Averaging Period
Qave Point Sources
Point Sources
CY2000-2010 Flows
Qave Nonpoint Sources
PS Avereraging
Period

## Slide 9: Precipitation and Growth
There are two signals from flow:
  “Random noise” from natural variation in precipitation.
  An increasing trend from growth.
The noise should be factored out to clarify progress.
The increase due to growth is an important factor that should be made apparent.
Growth
  Load differences in similar flow years can be attributable to growth and are consistent with estimates of population growth and EDUs from the Maryland Department of Planning.
  However, TN Load decreased reflecting WWTP upgrades and showing Progress.
  In wet years, this Progress is masked by rainfall.

## Slide 10
Precipitation, WWTP Flows and Growth
2001
WWTP Flow = 515 mgd
TN Load = 14.94 M lb
2007
WWTP Flow = 536 mgd
TN Load 12.67 M lb
2001
Precip = 37.43 inches
2007
Precip = 37.62 inches
WWTP Annual Flows CY* 2000 - 2010
2008
WWTP Flow = 592 mgd
TN Load 13.25 M lb
Precip = 45.77 inches
2008
Maryland Annual Average Precipitation CY* 2000 - 2010
*The charts above were developed using calendar year data, and are presented with the purpose of showing the correlation between rainfall and WWTP flows

## Slide 11
Annual Flows for
Major WWTPs
Annual TN Load for Major WWTPs:
Significant reduction after 2005
Reflecting ENR upgrades
Load is reduced despite increase flows from hookups or growth, but progress is hidden by rainfall
Flows vs Loads – Major WWTPs

## Slide 12
Annual Flow Weighted
TN Concentrations
Trend – When presentation is flow-weighted, the trend becomes apparent.
Annual Flows for
Major WWTPs Facilities
Flows vs TN Concentrations – Major WWTPs

## Slide 13
Flows vs TP Concentrations – Major Facilities
Annual Flows for
Major WWTPs Facilities
Annual Flow Weighted
TN Concentrations
Trend – When presentation is flow-weighted, the trend becomes apparent.

## Slide 14: Conclusion
The 2009 Executive Council (EC) intended to measure progress of implementation (report “Practices in Place”)
Current indicator does not show Progress because:
  It is confounded by rainfall
  Is inconsistent with NPS progress reporting
Progress reporting requires a consistent flow averaging period for both PS and NPS
If current indicator is retained, other indicators not confounded by rainfall are needed, including:
  WWTP performance (Nutrient concentrations)
  Normalized or average flows for load estimates
  Number of facilities upgraded