## Slide 1: The Control File
The control file contains the parameters used to run CE-QUAL-ICM. It consists of card images 80 characters in length. The for­mat of the input files has been develop­ed in order to take advan­tage of a full-screen text editor. The control file begins with six lines, which can be used for file iden­tification and are ig­nored by the program. The rest of the file consists of a line, which con­tains the card identifi­ca­tion and the names of the FORTRAN vari­ables as­sociated with the input card. The FORTRAN names are right-justified according to the field widths asso­ciated with the input vari­able. The next line consists of the actual input values. There are 10 input fields associ­ated with each card although the first field is not used. Each field has a length of eight charac­ters. The next line is left blank for ease of display in a full-screen edi­tor.
There are no optional cards in the control file - each card is required although there may be no values as­sociated with the card. The following pages contain a descrip­tion of each card. All charac­ter inputs must be capitalized except the TITLE cards or the variable will take on the default value.

## Slide 2: HYDC Options
BINARY – Three dimensional binary input, Z-grid
ASCII – Text input, 1, 2, or 3 dimensions
DEPTH_AV – Two dimensional (longitudinal/lateral) binary input
SIGMA_HYDRO – Hardwired to .FALSE. in code. A switch to .TRUE. is compatible with EFDC

## Slide 3: Horizontal Diffusion (HDIFF)
Field Name Value Description
1 XYDF Real Value for horizontal diffusion (m2 s-1)
2 ZDFMUL Real Multiplier for vertical diffusion
The first application of the water-quality model was in a system with negligible horizontal dispersion. To minimize the size of the hydrodynamic file, dispersion was specified once in the control file rather than written out by the hydrodynamic model at every cell interface, at every time step. This feature is still in place when the BINARY or DEPTH_AV hydrodynamic options are employed. Spatially-variable dispersion is a feature of the model code but the user must perform revisions to read dispersion in binary format. When the ASCII option is employed, spatially- and temporally-varying horizontal dispersion is specified in the hydrodynamic file and the field on this card is ignored.

## Slide 4: Active Constituents (ACT CST)
Field Name Value Description
1-27 ACC Character Turns on/off constituent calculations
This card allows the user to turn on/off a state variable for a simula­tion. Care must be taken when exercising this option because of the interaction of the state variables in the kinetic formulations. This option can be used when initially calibrating the water-quality model transport to the hydro­dynamic model transport using salinity. This option turns off computations only. All state variables must still be included in load files, boundary conditions, etc.

## Slide 5
MODULE SIZES
C***** Parameter declarations
C***** CHESAPEAKE BAY 50,000 CELL MODEL /mnt/cercolx1/1994_HYDRO
INTEGER,PARAMETER :: NCP=36,
c . NBP=56920,
c . NQFP=147941,
c . NHQP=102085,
c . NSQFP=20439,
c . NSBP=11064,

## Slide 6
CNAME(1) = 'Temperature'
CNAME(2) = 'Salinity'
CNAME(3) = 'Inorganic Solids'
CNAME(4) = 'Algal Group 1'
CNAME(5) = 'Algal Group 2'
CNAME(6) = 'Algal Group 3'
CNAME(7) = 'Zooplankton Group 1'
CNAME(8) = 'Zooplankton Group 2'
CNAME(9) = 'Labile DOC'
CNAME(10) = 'Refractory DOC'
CNAME(11) = 'Labile POC'
CNAME(12) = 'Refractory POC'
CNAME(13) = 'Ammonium'
CNAME(14) = 'Nitrate-nitrite'
CNAME(15) = 'Urea'
CNAME(16) = 'Labile DON'
CNAME(17) = 'Refractory DON'
CNAME(18) = 'Labile PON'
CNAME(19) = 'Refractory PON'
CNAME(20) = 'Total phosphate'
CNAME(21) = 'Labile DOP'
CNAME(22) = 'Refractory DOP'
CNAME(23) = 'Labile POP'
CNAME(24) = 'Refractory POP'
CNAME(25) = 'Particulate Inorganic P'
CNAME(26) = 'COD'
CNAME(27) = 'Dissolved oxygen'
CNAME(28) = 'Particulate silica '
CNAME(29) = 'Dissolved silica'
CNAME(30) = 'G3POC'
CNAME(31) = 'G3PON'
CNAME(32) = 'G3POP'
CNAME(33) = 'Clay'
CNAME(34) = 'Silt'
CNAME(35) = 'Sand'
CNAME(36) = 'Org Sed'

## Slide 7
Table 2-1 Water Quality Model State Variables | 
Temperature | Salinity
Fixed Solids | Freshwater Algae
Spring Diatoms | Other (Green) Algae
Dissolved Organic Carbon | Labile Particulate Organic Carbon
Refractory Particulate Organic Carbon | G3 Particulate Organic Carbon
Ammonium | Nitrate+Nitrite
Dissolved Organic Nitrogen | Labile Particulate Organic Nitrogen
Refractory Particulate Organic Nitrogen | G3 Particulate Organic Nitrogen
Phosphate | Dissolved Organic Phosphorus
Labile Particulate Organic Phosphorus | Refractory Particulate Organic Phosphorus
G3 Particulate Organic Phosphorus | Particulate Inorganic Phosphorus
Chemical Oxygen Demand | Dissolved Oxygen

## Slide 8: NXCBC, NXHDR, NXS1, etc.
The code reads ahead to see when the next update to boundary conditions, loads, etc. occurs. There should be one set of inputs beyond the termination of the model run. Either add a dummy day at the end of a single input file or add a dummy file in the case of multiple input files.

## Slide 9: External Loads Files
Three files are available for the input of external loads. The format of the files is identical. Provision of three files allows separation of loads by source e.g. point-source and nonpoint-source. Three files also allow updates of loads at different time intervals. One file can list loads at daily intervals while the others lists loads at monthly intervals.
The first two lines in each External Loads file are reserved for identification. The remainder of each file lists the number of loads for each constituent, the cell location for each load, and the loading rate for each cell. Multiple inputs into single cells are allowed. Once specified, loads are held constant until updated. Loads may be updated at arbitrary intervals. The total number of loads and their location can only be altered by reading a new input file. In practice we rarely do this.

## Slide 10: External Loads Files
NPSLN = NCP You must specify the number of loads for the number of constituents specified in the MODULES statement (36 for Chesapeake Bay).
NPSLB is specified for the number of active constituents (NAC = 28 for Chesapeake Bay). You must specifiy NPSLB even if a constituent has no loads e.g. temperature.
Loads must be specified for all active constituents, even if there is no load. In that case, the load is zero.

## Slide 11: The Boundary Conditions File
This file specifies boundary concentrations for all constituents at each boundary face. The file consists of three portions. The first three lines contain header information skipped over by a FORMAT statement. Next, the number of flow faces that are open boundaries is specified. Then the boundary concentrations are input.
The number specified for boundary faces must agree with the number of boundary faces in the map file. These are indicated by pairs of zeroes for the ILB (I left box) and IB (I box) or for JB (J box) and JRB (J right box). The boundary concentrations are entered in the order in which they are encountered within the model code. This is the same order in which the zero pairs occur in the map file. When ICM is coupled to CH3D, the faces are ordered along one CH3D axis, then along the other axis, for each level from surface to bottom. This convention can be awkward. Usually, a preprocessor is employed to translate between convenient boundary specification (e.g. by location or source) and the model format. Boundary concentrations must be specified for each of the active constituents (NAC = 28 for Chesapeake Bay).

## Slide 12: The Boundary Conditions File
As with loads, boundary conditions remain constant until updated.
Our convention is to specify loads of carbon, nitrogen, phosphorus, and solids at river inflows. In this case, boundary concentrations are specified as zero so that loads are not input twice. Our convention is not a rule, however. The user may specify pollutant concentrations at inflows, if desired.
Concentrations of all substances are conventionally specified at open boundaries such as the junction between an estuary and the ocean.