## Slide 1: Partial Attenuation Model
Potential indicators of solids include Total Suspended Solids (TSS), Volatile Suspended Solids (VSS), Fixed Solids (FSS), Chlorophyll (CHL), and Particulate Organic Carbon (POC).
Potential indicators of color include Dissolved Organic Carbon (DOC) and Salinity (SALT).
The background attenuation can be locally adjusted.

## Slide 2: Partial Attenuation Model
Stepwise regression was employed to evaluate additive models which included various combinations of contributing factors. Superior results (R2 = 0.623) were obtained for a simple model which related KE to TSS and SALT:
in which:
Ke = coefficient of diffuse light attenuation (m-1)
a1 = background attenuation (m-1)
a2 = attenuation by total suspended solids (m2 g-1)
a3 = relationship between attenuation and salinity (m2 kg-1)
TSS = total suspended solids concentration (g m-3)
SALT = salinity (kg m-3)

## Slide 3: Partial Attenuation Model
Parameter values obtained from regression were: a1 = 1.647 m-1; a2 = 0.0557 m2 g-1; a3 = -0.0624 m2 kg-1. The negative value for a3 implies that freshwater is more highly-colored than ocean water.
Examination of residuals indicated:
Negative residuals (observed attenuation less than modeled) near the James, Rappahannock, Potomac and Susquehanna fall lines.
Negative residuals in the lower Potomac and St. Marys River.
Positive residuals (observed attenuation greater than modeled) in the York and Mattaponi rivers.
Positive residuals in the lower James and Elizabeth Rivers.

## Slide 4: Partial Attenuation Model
Observed TSS in the attenuation relationship is the sum of organic and inorganic particulate matter.
Concentration of inorganic solids is obtained from the WQM as the sum of the fine clay, clay, silt, and sand state variables.
Observed organic (volatile) solids correspond to model POC state variables. Model POC is the sum of the three algal groups and three particulate organic carbon variables.
Organic solids = 2.9 * POC (R2 = 0.889).
To avoid negative values, a minimum Ke value of 0.15 m-1 is imposed.

## Slide 5: Some Practical Details
In order to use existing code, our input file allows for attenuation from chlorophyll. We specify the value zero.
Our code allows for different specification of attenuation from fixed and volatile solids. Since our relationship employs total suspended solids, we use the same value for fixed and volatile solids.
Our code allows for spatial variation of background attenuation. We use this option.
Our code allows for spatial variation of attenuation from solids. We use uniform values throughout.
If the spatially varying option is employed, values must be provided for each surface cell (≈ 11,000).