## Slide 1
Table 6-1 Constituents in Watershed and Water Quality Models |  | 
WSM Variable | Maps to | WQM Variable
Ammonium | ------> | Ammonium
Nitrate | ------> | Nitrate
Organic Nitrogen | ------> | Dissolved Organic Nitrogen, Labile Particulate Organic Nitrogen, Refractory Particulate Organic Nitrogen, G3 Particulate Organic Nitrogen
Dissolved Phosphate | ------> | Phosphate
Organic Phosphorus plus Particulate Inorganic Phosphorus | ------> | Dissolved Organic Phosphorus, Particulate Inorganic Phosphorus, Labile Particulate Organic Phosphorus, Refractory Particulate Organic Phosphorus, G3 Particulate Organic Phosphorus

## Slide 2: Routing watershed model organic nitrogen into water quality model state variables

## Slide 3: Dissolved organic nitrogen concentration at Station CB1.1, below Susquehanna River inflow
Note lack of relationship to flow.

## Slide 4: Splits of particulate organic nitrogen into reactive classes
For the Susquehanna River, the reactive splits are influenced by flow above 6,500 m3 s-1. The relationships used to determine the reactive classes are of the form:
(1)
(2)
(3)
in which:
Fg1 = labile fraction of particulate organic nitrogen (0 < Fg1 < 1)
Fg2 = refractory fraction of particulate organic nitrogen (0 < Fg2 < 1)
Fg3 = G3 fraction of particulate organic nitrogen (0 < Fg3 < 1)
α1 = Effect of flow > 6,500 m3 s-1 on Fg1 (s m-3)
α2 = Effect of flow > 6,500 m3 s-1 on Fg2 (s m-3)
Q = Flow at Conowingo outfall (m3 s-1)

## Slide 5: Routing watershed model organic and particulate inorganic phosphorus into water quality model state variables

## Slide 6: There are a lot of splits
Dissolved vs. Particulate – based on observations at most upstream monitoring station.
PIP vs POP – based on fall-line observations.
Reactive classes of POP – relationships analogous to organic nitrogen.
Particulate inorganic phosphorus vs. particulate phosphorus at Susquehanna River fall line.

## Slide 7: Organic Carbon
The WSM has no state variable corresponding to the WQM organic carbon suite. Watershed organic carbon loads are derived by ratio to organic nitrogen.
The ratios (C:N ≈ 8) were derived from observations at the river inputs and are adapted here from the 2010 TMDL model (Cerco et al. 2010).
The distribution of watershed organic carbon into WQM state variables is analogous to the process for organic nitrogen. First, organic carbon is split into dissolved and particulate forms. Then the particulate organic carbon is routed into three reaction classes. The splits between particulate and dissolved form are the same as for organic nitrogen.
Routing of particulate organic carbon into reaction classes is conducted via relationships analogous to organic nitrogen.

## Slide 8: Other Loading Sources
Point-Source Loads
Shoreline Erosion
Atmospheric Deposition to Water Surface

## Slide 9: Boundary Conditions at Mouth

## Slide 10: Temperature
T = water temperature (oC)
Te = equilibrium temperature (oC)
KT = Heat exchange coefficient (watt m-2 oC-1)
Cp = specific heat of water (4200 watt s kg-1 oC-1)
ρ = density of water (1000 kg m-3)
H = thickness of model surface layer
The only source or sink of temperature considered is exchange with the atmosphere. Atmospheric exchange is considered proportional to the temperature difference between the water surface and a theoretical equilibrium temperature

## Slide 11: make_daily_hex.f
Inputs
Dry-bulb temperature (oC)
Wet-bulb temperature (oC)
Dew point (oC)
Wind speed measured 7 m above water surface (m/s)
Fractional sky cover (eighths)
Latitude (degrees) is hard-wired in program.

## Slide 12: make_daily_hex.f
Considerations
Your biggest headache is finding a consistent data set that extends the duration of your simulation.
You have no control over the height of wind speed measurements. Maybe not critical.
Wind speed over water will differ from wind speed measured over land (e.g. at an airport).
The program multiplies input wind speed by 1.5 to correct for inputs measured at an airport. This can be removed if you have in-situ measures.
Be careful of units of sky cover. The program uses eighths.
Wet bulb temperature is relic input. Not used.

## Slide 13: make_daily_hex.f
Outputs
Surface heat transfer coefficient (watt m-2 oC-1)
Equilibrium temperature (oC)
Photosynthetically active radiation (einstein/d)
Fractional daylength (0 < FD < 1)
Windspeed (m/s)

## Slide 14: make_daily_hex.f
Considerations
PAR is derived from computed daily average solar radiation.
The relationship is empirical based on measures in the Chesapeake Bay region. If you have observations of PAR, you may substitute these in the output.
FD is used to compute instantaneous irradiance from daily total.
Windspeed is used to compute reaeration if this option is selected..

## Slide 15: Irradiance
Irradiance at the water surface is evaluated at each model time step. Instantaneous irradiance is computed by fitting a sin function to daily total irradiance
Io = irradiance at water surface (E m-2 d-1)
IT = daily total irradiance (E m-2) FD = fractional daylength (0 < FD < 1)
DSSR = time since sunrise (d)