## Slide 1: Technical Appendix for Animal Mortality BMPs
June 1, 2023
Watershed Technical Workgroup,
Chesapeake Bay Partnership
Notes: The purpose of this technical appendix is to describe how the Animal Mortality BMP expert panel’s recommendations will be integrated into NEIEN, CAST and the Watershed Model. This involves how a load source reduction value for animal mortality BMPs can be incorporated as an approved BMP in the next version of CAST. Some aspects of the panel’s recommendations may not be applicable until Phase 7 of the Watershed Model.
Given Ruth’s explanation of the CAST schedule, with these Expert Panel recommendations being approved in the next month, the practices can be incorporated as BMPs into the next version of CAST.
Previously, it would not be an approved BMP. With an expectation of full Expert Panel recommendations being approved in Fall 2023, the practices can be incorporated as planning BMPs in CAST-21. Some aspects of the panel’s recommendations may not be applicable until Phase 7 of the Watershed Model.

## Slide 2: Proposed BMP Adjustment
The previously existing Mortality Composters BMP will be replaced with the new Animal Mortality Disposal by Composting practice.
The current planning-only BMP for broiler mortality freezers will be eliminated and replaced in favor of the rendering BMP, which includes the use of freezers or refrigeration units to store mortalities prior to transfer to the rendering facility.
Notes: So again as a brief overview of the panel's recommendations, the previously existing Mortality Composters BMP will be replaced with the new Animal Mortality Disposal by Composting practice. Additionally, the current planning-only BMP for broiler mortality freezers will be eliminated and replaced in favor of the rendering BMP, which includes the use of freezers or refrigeration units to store mortalities prior to transfer to the rendering facility. All the other details of that breakout are available within that TA.

## Slide 3: Summary of Received Feedback
One of the premises of the Expert Panel was to identify a baseline condition from which to measure the nutrient reduction effectiveness values for each of the defined BMPs.
The current technical appendix draft includes language which includes burial as a BMP, as well as a baseline practice. The practice can only serve as one or the other, and in this case it should only be reflected as a baseline condition. It is recommended that this change be reflected in a revised document for review.
Burial is a baseline practice so as such, it should not be reported.
Notes: We received great feedback from the group and so despite this accelerated CAST version schedule, we do not want to rush through this approval process so thank you for your thoughtful insight. This summary of feedback is that burial be shifted from a BMP to a baseline condition. It receives no credit in the model and is not allowed in many parts of the watershed, if not all of them.
I also want to mention that we received feedback that further work to see how this can be incorporated into Phase 7 would be worthwhile. While this TA will support near-term crediting, we can use Phase 7 to further adjust this as needed to fit what is happening in the watershed.

## Slide 4: Detailed Definitions of Mortality Practices
Practices below will replace previous practices with respective efficiency values. Efficiency values on next slide.
BASELINE:
  Animal mortality disposal by burial is the handling and disposal of poultry, livestock, or other routine animal mortalities by placing the carcass or carcasses below ground into an excavated pit, hole, or trench, which is then covered or capped. -baseline practice
Recommended BMPS:
  Animal mortality disposal by landfill or rendering is the handling, storage and disposal of poultry, livestock, or other routine animal mortalities by internment in a landfill or processing at a rendering facility.
  Animal mortality disposal by incineration is the handling, storage and disposal of poultry, livestock or other routine animal mortalities by thermochemical conversion using combustion, gasification, pyrolysis, or some combination of those methods. The methods result in gaseous and solid byproducts. It is expected that most nitrogen is transformed and lost to the atmosphere, while all phosphorus remains available for land application or transport.
  Animal mortality disposal by composting is the handling, storage and disposal of poultry, livestock or other routine animal mortalities by composting including one or more of the following, alone or in combination: static piles and windrows (a.k.a. passive piles), turned windrows, static aerated windrows, a bin system, a tunnel composter, or in-vessel composter such as a rotating drum.
    Units: Report units of animal units or tons of carcasses of dead animal for an annual practice or in units of systems for a structural system.
Notes: We have provided the definitions for these practices from the TA on this slide. This reflects the suggested feedback and adjustments to what is a baseline versus what is a bmp. You can see we have moved burial to a baseline practice and the other three practices would be credited within the model with load reductions.
All of these bmps are reported in units of AUs or tons of carcasses of dead animal for an annual practice, or in units of systems for structural systems.

## Slide 5: Efficiency Values for Practices
Pollutant | Burial | Compost | Incineration | Rendering
TN | 0 | 0.124% | 0.372% | 0.372%
TP | 0 | 0.059% | 0.059% | 0.059%
TSS | N/A | N/A | N/A | N/A
Notes: As you know this practice affects Nitrogen and Phosphorus but not sediment so see the associated efficiency values for each of the three BMPS as compared to the old baseline practice that receives no credit in the model.
As a reminder, these percentage reductions are on animal units or tons of carcasses of dead animal for an annual practice or in units of systems for a structural system.

## Slide 6: What types of projects are eligible to receive future credit?
Any mortality management practice or method mentioned that meets the definitions above in Q1/A1 and treats routine animal mortalities from one of the animal groups listed in Table B.2 above are eligible.
Practices or methods used for catastrophic mortality events are not eligible under this set of practices. Practices or methods that are also used to treat manure should not be reported twice, i.e., they should not be reported as both mortality and manure treatment practices.
Notes: Catastrophic deaths are not allowed to be reported as they do not represent the average expected mortality within the watershed. Practices that are also treating this manure should not be double reported

## Slide 7: Approval Timeline
TBD, these dates are subject to change***
  AgWG June for presentation on updated appendix
  WTWG July for approval
  WQGIT July/August for approval
  Late September inclusion into new model.

## Slide 8: Further Feedback/Discussion?