## Slide 1: WQGIT Recommendations on Climate Allocations
May 26, 2020
Water Quality Goal Implementation Team Conference Call

## Slide 2: WQGIT Decisions to Date

## Slide 3: Requested WQGIT Climate Allocation Recommendations to the Management Board
WWTP responsibility
  Only non-WWTP sources
  Include WWTP
Watershed loads first
  Take out jurisdiction loads first
  Do not consider jurisdiction loads
Year
  2025
  2035
Open Water (Confirm April Recommendation)
  How to deal with open water violations in the lower Bay

## Slide 4: WWTP responsibility
Increased effort can be allocated based on increased effort for non-WWTP loads or based on all loads
Loads are specified by state-basin, not by source. Adding WWTP responsibility does not mean that jurisdictions must get reductions from WWTP, just jurisdictions with high WWTP loads will have to do more
MD, VA, DC do more with All Loads / DE, NY, PA, WV do less with All Loads
Total reduction needed is higher because WWTP loads are in less-effective areas

## Slide 5: Watershed Loads First
Ran WQSTM run to show reduced non-attainment for jurisdiction reductions equal to the climate load increase
Allocated remaining effect
+
=
2025, phosphorus, OWDWDC, non-WWTP example

## Slide 6: Year
What change to account for:
  1995-2025
  1995-2035
When the reductions would need to be accomplished:
  2025
  2035
  Some other date
WQGIT previously discussed using the same year to account for the climate change and when the reductions would need to be accomplished

## Slide 7: Open Water Decision
Open water is an important use for living resources
Open water may be more affected by temperature due to concentrations closer to saturation
The Modeling Workgroup did not advocate for the WQGIT to drive allocations with CB6 and CB7 open water
  Relatively insensitive to load reductions
  No other Mainstem Open Water violations through 2055
    Other large rivers mostly have no violations through 2055
  Strong dependence on the appropriate delineation between ‘Open Water over Deep Water’ and ‘Open Water to the bottom’
The WQGIT decided to not include Open Water in the climate allocations pending CBF consideration

## Slide 8: Nitrogen Total Reductions
2035 increases effort substantially
Including WWTP increases necessary reductions
Watershed loads first are a little lower for N

## Slide 9: Phosphorus Total Reductions
2035 increases effort substantially
Including WWTP increases necessary reductions
Watershed loads first is a larger reduction for P

## Slide 10: Requested WQGIT Climate Allocation Recommendations to the Management Board
WWTP responsibility
  Only non-WWTP sources
      OR
  Include WWTP
Watershed loads first
  Take out jurisdiction loads first
      OR
  Do not consider jurisdiction loads
Year
  2025
  OR
  2035
Open Water (Confirm April Recommendation)
  Do not include Open Water