## Slide 1: AgWG Ad Hoc CAST Issues
January 13, 2021

## Slide 2: CAST-21 Workplan (Working Draft) *Approved data and method changes need to be finalized through the WQGIT by Sept. 1, 2021*
KEY ACTION | STATUS
Task 1: Updates to data & methods that typically occur every 2 years. | On-going In process: “Rules of the Road” document for data submissions
Task 2: Investigate alternative forecasting methods for ag land uses & animals | Nov 19 AgWG: CBPO presentation on 4 methods of forecasting Return Feb/March 2021 for decision
Task 3: Investigate 2012-2017 Ag Census change for fallow/idle acres | AgWG Sept 17; NASS consulted; no new information; No further action; TASK COMPLETED? decision Jan AgWG
Task 4: Investigate use of latest landcover & LiDAR imagery to better define changes in total ag (& other land use) acres | Oct 15 AgWG: P. Claggett, USGS & J. Czawlytko, Chesapeake Conservancy; seeking feedback Jan AgWG; Feb 2021 for decision
Task 5: Investigate alternatives for double-crop acre estimates | Oct 15 AgWG; NASS consulted- no new information; No further action; TASK COMPLETED? Decision Feb AgWG
Task 6: Consider supplemental NM for soybeans | In process Dec Ad Hoc; Jan Ad Hoc discussion
Task 7: QA/QC’d historic & current layer pop. data for Hillandale Farms (PA) | In process Feb Ad Hoc- general discussion
Task 8: Build-in Verification Ad Hoc Team products | In process
Questions/Comments?
TODAY

## Slide 3: NM Supplemental Percent Reductions (Only after Core NM is applied)
Data provided by Phase 6.0 Nutrient Management Expert Panel
CRITICAL CONCEPT:
Supplemental NM is applied to Edge of Stream Delivery

## Slide 4: What is driving these N load concerns?
Agricultural Loading Rates? VA
Ag Census (i.e. Source Of Crop Data) DE
The NM BMP Recommendations? PA
  NM Expert Panel Members (Phase 6)
    Response From 2 of 6
    Changed Professional Status, Lack Context (it’s been 5 or 6 years…)
  Changing An Approved EP Recommendation Must Follow Science (BMP protocol)
    Protocol for the Development, Review, and Approval of Loading and Effectiveness Estimates for Nutrient and Sediment Controls in the Chesapeake Bay Watershed Model

## Slide 5: Agricultural Loading Rates
Based on available literature & best professional judgement
“N losses from soybeans are only somewhat lower than corn, because N fixation inputs (which are poorly characterized) are apparently substituting for fertilizer inputs.” (p.11)

## Slide 6: Census of Agriculture
Accuracy of Ag Census crop acres questioned
  spatially distributed land use from the Land Cover/Land Use data team starting with the CAST-21 could be an improvement
Method of modeling double-crop soybeans approved by CBP partnership
  Determined sound by USDA-NASS

## Slide 7: NM Expert Panel Recommendations
Soybeans NM controlling for P (not N)
LGUs do not recommend N application on soybeans BUT…
  Real-world N application occur
  Crop Application Goal @ 0.12 lbs N/bu  CBW avg 3.58 lbs N/ac
Core N NM available
  Reduces modeled N application
Supplemental N NM NOT available
  Timing & Placement of excess N irrelevant (still subject to loss)
  Rate? Excess N reduced is still excess N subject to loss…

## Slide 8: Soybean Crop Application Goal
Full Season Soybeans
0.12 lbs N/bu (~5.7 lbs N/ac)
CBW Average: (~3.58 lb/N ac)
UME, Penn State, VT recommend zero N application
Double Cropped Soybeans
Zero N applications
UME, Penn State, VT recommend zero N application
Assumption: “Nitrogen application is not recommended for soybean production, however, use of commercially available fertilizer formulations may result in application of up to 50 lb N / acre when fertilizer formulation and application rate is determined by crop P2O5, K2O, S, or other nutrient needs. Organic waste nitrogen application to full-season soybean is not recommended because it is an agronomically inefficient use of applied nutrients. Organic wastes should only be applied to small grain - double-crop soybean rotations at rates and timings to supply the recommended nitrogen rate to the small grain crop.” – UME SFM-1

## Slide 9: Application Goal Multipliers
Land Use | Non NM N Multiplier | NM N Multiplier | Non NM P Multiplier | NM P Multiplier
Full Season Soybeans | 1.2 | 1.0 | 1.5 | 1.0
Grain with Manure | 1.3 | 1.0 | 3 | 1.0
Grain without Manure | 1.2 | 1.0 | 1.5 | 1.0
Legume Hay | 1.2 | 1.0 | 1 | 1.0
Silage with Manure | 1.4 | 1.0 | 3 | 1.0
Silage without Manure | 1.2 | 1.0 | 1.5 | 1.0
Small Grains and Grains | 1.2 | 1.0 | 1.5 | 1.0
Small Grains and Soybeans | 1.2 | 1.0 | 1.5 | 1.0
Specialty Crop High | 1.3 | 1.0 | 2 | 1.0
Specialty Crop Low | 1.2 | 1.0 | 2 | 1.0
Other Agronomic Crops | 1.1 | 1.0 | 1.5 | 1.0
Other Hay | 1 | 1.0 | 1 | 1.0
Pasture | 1 | 1.0 | 1 | 1.0
Data provided by Phase 6.0 Nutrient Management Expert Panel
Full Season Soybeans:
40 bu/ac @ 100 ac
Core NM:
40 bu/ac x 0.12 lbs N/bu x 1.0 x 100 ac =
480 lbs N applied
40 bu/ac x 0.33 lbs P/bu x 1.0 x 100 ac =
1,320 lbs P applied
Non NM:
40 bu/ac x 0.12 lbs N/ac x 1.2 x 100 ac =
570 lbs N applied
40 bu/ac x 0.33 lbs P/bu x 1.5 x 100 ac =
1,980 lbs P applied
CRITICAL CONCEPT:
Multipliers are applied to Crop Application Goal

## Slide 10: Crop Application Goal on Major Crops lbs of N/Year = State-Supplied lbs of N/Application Goal Yield Unit/Year X Yield/Year X 1.1*
Crop | DoubleCrop | Nutrient | Yield Unit | DE_1 | MD_1 | NY_1 | PA_1 | VA_1 | WV_1
Alfalfa Hay Harvested Area | N | TN | dry tons | 1 | 1 | 1 | 1 | 1 | 1
Alfalfa Hay Harvested Area | N | TP | dry tons | 5 | 5 | 5 | 6 | 5 | 5
Corn for Grain Harvested Area | N | TN | bushels | 0.92 | 0.92 | 0.92 | 0.92 | 0.92 | 0.92
Corn for Grain Harvested Area | N | TP | bushels | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
Corn for Grain Harvested Area | Y | TN | bushels | 0.92 | 0.92 | 0.92 | 0.92 | 0.92 | 0.92
Corn for Grain Harvested Area | Y | TP | bushels | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
Wheat for Grain Harvested Area | N | TP | bushels | 0.31 | 0.31 | 0.31 | 0.31 | 0.31 | 0.31
Wheat for Grain Harvested Area | N | TN | bushels | 1.25 | 1.25 | 1 | 1 | 1.25 | 1.25
Wheat for Grain Harvested Area | Y | TP | bushels | 0.465 | 0.465 | 0.465 | 0.465 | 0.465 | 0.465
Wheat for Grain Harvested Area | Y | TN | bushels | 1.25 | 1.25 | 1 | 1 | 1.25 | 1.25
Pastureland and rangeland other than cropland and woodland pastured Area | N | TN | acres | 15 | 15 | 15 | 15 | 15 | 15
Pastureland and rangeland other than cropland and woodland pastured Area | N | TP | acres | 4 | 4 | 4 | 4 | 4 | 4
Soybeans for beans Harvested Area | N | TN | bushels | 0.12 | 0.12 | 0.12 | 0.12 | 0.12 | 0.12
Soybeans for beans Harvested Area | N | TP | bushels | 0.33 | 0.33 | 0.33 | 0.33 | 0.33 | 0.33
Soybeans for beans Harvested Area | Y | TN | bushels | 0 | 0 | 0 | 0 | 0 | 0
Soybeans for beans Harvested Area | Y | TP | bushels | 0 | 0 | 0 | 0 | 0 | 0
Data provided by states after consultation with nutrient management program staff.
Chesapeake Bay Program Phase 6 Beta 3 Watershed Model Webinar
July 11, 2016
CRITICAL CONTEXT:
“Crop Application Goal” assumes Core NM is in place
Full Season Beans receive
0.12 lb N/bu
&
0.33 lb P/bu
Double Crop Beans
0 lb N/bu
&
0 lb P/bu
NM on full season beans is controlling/managing for phosphorus!
*AMS elected to multiply yearly yield by 1.1 assuming farmers are optimistic, and average yields are often under-estimated.
Crop Application Goal

## Slide 11
1.Define Crop Application Goal
A
Crop Application Goal/Yield Unit
B Yields/Acre
C
Acres
Crop Application Goal
2. Define Manure Available to Crops
Manure Generated
Direct Deposition on Pasture
Direct Deposition to Riparian Pasture Areas
Deposited within Barnyard
Storage and Handling Loss
Stored Manure
Manure Transport
Feed Additive BMPs
Volatilization
Available for Application
Barnyard BMPs
Ammonia Reduction BMPs
Available for Transport
Mineralization
3. Spread Manure to Crops
4. Define Inorganic Fertilizer Available to Crops
5. Spread Fertilizer to Crops
Ag Census or
NASS Annual Surveys
(Animal populations dictate manure load estimates)
A AMS
B NASS Annual Survey
C Ag Census
AAPFCO Fertilizer Sales Data
Allocation of Ag Nutrients in the Watershed Model
AMS= Agricultural Modeling Subcommittee

## Slide 12
Animal Data
Animal Populations: explore other estimating options (MD/NY; Task 1)
Crop Production/Acres
Crop Production Acres: improve annual estimates (MD; Task 1)
Nutrient Applications/Assumptions
Fertilizer Sales and Use Data (MD; Task 1)
BMP Tracking & Reporting
Dairy Precision Feeding (PA)
Heavy Use Area Protection- NRCS 561 (NY?)
BMP Effectiveness/Modeling
Winter Crop (NY/PA)
Manure Transport / Manure Treatment Technologies (PA)

## Slide 13
Animal Data
Animal Populations: explore other estimating options (MD/NY; Task 1)
Crop Production/Acres
Crop Production Acres: improve annual estimates (MD; Task 1)
Nutrient Applications/Assumptions
Fertilizer Sales and Use Data (MD; Task 1)

## Slide 14: Improving Ag Data? (TASK 1)
CRITICAL CONCEPT:
To maintain integrity of CBWM there are two options for new data sets:
Provide data all the way back through 1985.
OR
Use the trend in new data sets for the years available.
CBWM= Chesapeake Bay Watershed Model
Crop Acreage Data
Alternative methods to account for fitting Ag Census data to CBP needs?
  Adjusting methods for estimating crop acres (e.g. double crops)
Alternative/supplemental data sets
  Other data sets at the state or federal level?
Animal Population Data
Additional NASS Annual Survey Data may be available to inform population trends between census years (incorporated every two years)
  Dairy, Beef Cattle, Layers, Swine…
Direct from industry data can inform animal population trends between census years.
  Requires careful cooperation
  Legal, privacy assurances
Other Data Issues (new data incorporation every 2 years)
Soil P data
  Gary Shenk Sept 2018 presentation to AgWG on data set incorporated into the CBWM
  Additional soil P data is welcome and encouraged (NY & WV have made inquiries)
Manure Nutrient Concentration Data
  Changes in management may result in changes in nutrient concentrations
  Additional manure concentration data is welcome and encouraged
  Fertilizer Data
  More accurate allocation of fertilizer within the CBW?
    Jurisdictions working with state chemists
Crop Application Goal
Manure Generated
4. Define Inorganic Fertilizer Available to Crops
UPDATES?

## Slide 15
BMP Tracking & Reporting
Dairy Precision Feeding (PA)
Heavy Use Area Protection- NRCS 561 (NY?)

## Slide 16
BMP Effectiveness/Modeling
Winter Crop (NY/PA/MD)
Manure Transport / Manure Treatment Technologies (PA/MD)

## Slide 17
Jan 21st AgWG
  Charlie White (Winter Crop BMP)
  Peter Claggett Landcover/ LiDAR Data (Task 4)
Feb Ad Hoc:
  Hillandale (Task 8) Discussion
Feb AgWG:
  Decision Landcover/ LiDAR Data (Task 4)
  Decision Double Crop methods (Task 5)
March AgWG
  Decision Forecasting Ag Trends (Task 2)

## Slide 18
BMP Concern | CBP BMP Effectiveness Source | Next Steps
Dairy Precision Feeding (PA) | Definitions and reductions approved by the WQGIT in 2009 | PA Action Team
Rotational/Prescribed Grazing (PA) | Definitions and benefits were reviewed and approved by the Agriculture Workgroup and WQGIT in 2010 | RESOLVED
Heavy Use Area Protection- NRCS 561 (PA) | Loafing Lot Management definitions and reductions approved by the Chesapeake Bay Program’s Nutrient Subcommittee in 2003. | ?
Nutrient Management on Pasture (NY/PA) | Nutrient Management Practices for use in the Phase 6.0 Chesapeake Bay Program Watershed Model (2016) | RESOLVED
Commodity Cover Crops (NY/PA) | Cover Crops Practices for use in Phase 6 of the Chesapeake Bay Watershed Model (2016) | EP Chair discussion with AgWG (Dec 2020)
Manure Transport / Manure Treatment Technologies (PA) | Manure Treatment Technologies: Recommendations from the Manure Treatment Technologies Expert Panel to the CBP’s WQGIT to define Manure Treatment Technologies as a Best Management Practice (2016) Manure Transport: definition and benefits have remained in use since review and approval by the CBP partnership’s source sector workgroups for tributary strategy development. | Work with MWG
Protocol for the Development, Review, and Approval of Loading and Effectiveness Estimates for Nutrient and Sediment Controls in the Chesapeake Bay Watershed Model

## Slide 20: Comments on CAST-19: Soybean nitrogen application (p.2)
With the increase in full-season soybeans and decrease in double cropped soybeans in CAST-19, the N application rates were examined. Chris Brosch-DDA, Jill Whitcomb-PA-DEP; James Martin-VA-DEQ

## Slide 21: Comments on CAST-19: Soybean nitrogen applicationResponse (p.3)
N applications on soybeans depend on whether the soybeans are full season or double cropped.
Double-cropped receive 0 N applications.
Full season have a N crop need of 0.12 lb./bu (5.70 lbs./ac)
  watershed-wide avg
    2.23 inorganic lbs./acre applied
    1.35 organic lbs./acre applied
The University of Maryland, Penn State, and Virginia Tech nutrient management guidelines recommend zero N on full-season or double-cropped soybeans.

## Slide 22: Comments on CAST-19: Soybean nitrogen application_Resolution (p.3)
A comparative analysis of changing full-season soybeans to corn and the resulting nitrogen loads was provided to PA-DEP.
The soybean N application and N fixation assumed for Lancaster County and the average in the rest of PA’s watershed were provided to Jill Whitcomb, PA-DEP.
The CBP will provide to Jill Whitcomb, PA-DEP, and other states the peer reviewed research and other sources that document nutrient runoff/leaching rates from legumes, and how it is applied in the modeling tools (e.g., is it a constant throughout the year or is there a difference in seasonality, is there a difference depending on what crop preceded/followed, etc.) by the May 25, 2020 WQGIT.
The AgWG will be asked to consider establishing a group to evaluate nutrient management BMPs for nitrogen on full season soybeans. [see Workplan Task 6]

## Slide 23: N Application on Soybeans
From Water Quality GIT presentation to Management Board 7/9/20

## Slide 24: Concern:
Full Season (under Core NM):
Assume 40 bu/ac @ 100 ac
40 bu/ac x 0.12 lbs N/bu x 1.0 x 100 ac =
480 lbs N applied
Double-Crop
Assume 25 bu/ac @ 100 ac
25 bu/ac x 0 lbs N/bu x 1.0 x 100 ac
0 lbs N applied (on beans)
N applied to sm grain
Model Assumption
CRITICAL CONCEPT:
N load attributed to soybean acres includes estimated leaching/runoff of residual N based on scientific literature review.
Agricultural Loading Rates
Ag Loading Rate Review Steering Committee
Nutrient management on full-season soybeans?
YES: “core NM”
  NO: “supplemental NM” for N rate, placement & timing
    Why? NM on soybeans is controlling for P…
Given the same acreage…
A shift from double-crop to full-season soybeans will result in an increase in attributed N load.

## Slide 25: Additional Concerns- MD
Animal Populations: explore other estimating options
  Improve livestock (dairy, equine, beef) population estimates
    Reduction goals for some counties unattainable due to inaccurate population assumptions (i.e. poultry mortality, waste management).
Crop Production Acres: improve annual estimates
  MD’s Nutrient Management Annual Implementation Report (AIR)
  other means (USDA-FSA crop reporting)
Fertilizer sales and use data
  Better understanding via state chemist

## Slide 26: Additional Concerns- NY
Animal Populations: explore other estimating options
  Over-estimation for counties partially within the watershed
Cover Crops:
  Additional category Commodity Cover Crops with Manure (not inorganic fertilizer).
    Encourage/credit cover cropping in forage-based dairy cropping systems
Nutrient Management on Pasture:
  Credit options and/or inorganic fertilizer rates

## Slide 27: Additional Concerns - PA
  Dairy Precision Feeding:
    Revisit the criteria for measurement of implementation
  Rotational/Prescribed Grazing:
    Revisit the criteria for determining implementation
  Cover Crops:
    Revisit the criteria for crediting commodity cover crop (harvested, nutrients applied)
  Manure Transport / Manure Treatment Technologies:
    Revisit the requirement to apply NM to offset an assumed “backfill” of inorganic application
      Assumption does not adequately reflect current practice
  Heavy Use Area Protection (NRCS 561):
    HUAP is not currently credited
    HUAP should be synonymous to Loafing Lot Management BMP
  Nutrient Management on Pasture:
    Crediting NM on pasture/non-cropland acres

## Slide 28
1.Define Crop Application Goal
A
Crop Application Goal/Yield Unit
B Yields/Acre
C
Acres
Crop Application Goal
2. Define Manure Available to Crops
Manure Generated
Direct Deposition on Pasture
Direct Deposition to Riparian Pasture Areas
Deposited within Barnyard
Storage and Handling Loss
Stored Manure
Manure Transport
Feed Additive BMPs
Volatilization
Available for Application
Barnyard BMPs
Ammonia Reduction BMPs
Available for Transport
Mineralization
3. Spread Manure to Crops
4. Define Inorganic Fertilizer Available to Crops
5. Spread Fertilizer to Crops
Ag Census or
NASS Annual Surveys
(Animal populations dictate manure load estimates)
A AMS
B NASS Annual Survey
C Ag Census
AAPFCO Fertilizer Sales Data
Allocation of Ag Nutrients in the Watershed Model
AMS= Agricultural Modeling Subcommittee
https://www.dreamstime.com/stock-images-square-peg-round-hole-image12777364

## Slide 29: Source for distribution of statewide populations can change.
  Example: Pennsylvania provides fraction of cattle in every county for the year 2019, and these fractions are used to distribute TOTAL statewide cattle populations from the Census of Agriculture.
Census
100 Cattle
County A
35%
Outside Watershed
15%
County C
50%
County B
0%
PA Data
(75 Cattle)
100 Cattle
County A
25%
Outside Watershed
25%
County C
40%
County B
10%
Source of TOTAL statewide populations will not change for Phase 6 Watershed Model.
CRITICAL CONCEPT