## Slide 1
Assessing oyster aquaculture impact on water quality in Chesapeake Bay
Richard Tian, Carl Cerco, Lewis Linker
Chesapeake Bay Program Office
Modeling Quarterly Review Meeting
04/11/2018
Annapolis

## Slide 2
Oyster Aquaculture Facts
Oyster aquaculture is on a trajectory of exponential expansion in Chesapeake Bay.
Increased by 10 folders from 2012 to 2016 in Maryland waters and more established on VA portion of the Bay.
By 2025, 112 millions oysters harvest projected in MD and 280 millions oyster harvest in VA.
Equivalent to an annual removal of 78x103 lbs nitrogen, and 8.6x103 lbs phosphorus.
On top of nutrient removal, oyster filtration can help to clean up the Bay.

## Slide 3
Oyster Basic Equation in Model
In which:
O = oyster biomass (g C m-2)
α = assimilation efficiency (0 < α < 1)
Fr = filtration rate (m3 g-1 C d-1)
TSS = Total Suspended Solids (g m-3)
IF = ingestion fraction (0 < IF < 1)
RF = respiration fraction (0 < RF < 1)
BM = basal metabolism (d-1)
β = mortality (d-1)
Carl Cerco; modified

## Slide 4
Cyanobacteria
Diatom
Green
L-RPOC
L-RPON
L-RPOP
ISS
PIP
OYSTER
L-RPOC
L-RPON
L-RPON
ISS
PIP
Bottom water
Sediment
Nutrient
Respiration
Fluxes generated by oyster

## Slide 5
Diagenesis Model with Benthos (Carl Cerco; Modified)
Particulate
Organic
Matter
Dissolved
Nutrients
Dissolved
Oxygen
Filter
Feeders
Particulate
Organic
Matter
Dissolved
Nutrients
Oxygen
Demand
transport
filtration
settling
biodeposits
sediment-water
exchange
excretion
sediment-oxygen
demand
diagenesis
diagenesis
Water
Column
Sediments
Burial
Denitrification
respiration

## Slide 6
Oyster Aquaculture sites
MD: Salinity ≥7 ppt, depth  12 ft.
VA: Lease sites
Sufficient phytoplankton and suspended solids
Model setup
392 million oysters harvest in 2025, equivalent to 468k lbs C in biomass.
78k lbs N and 8k lbs P reduction in nutrient loads.
Oyster biomass in the water column is 1.5 times the annual harvest for aquaculture in cages (20% in MD and 80% in VA).
Oyster biomass on the bottom is twice the annual harvest for bottom culture (80% in MD and 20% in VA).

## Slide 7
Impact on deep water and deep channel: non-attainment decreased from 6.00 to 5.24%, to 1.2 million pounds of nitrogen and 22 thousand pounds of phosphorus removal from the watershed
No significant difference between base and WIP scenarios.
Deep Channel criteria assessment

## Slide 8
Local open water seems less impacted
Open water criteria assessment
(Examples with oyster aquaculture)

## Slide 9
Difference in Hypoxia volume in the whole Bay
(DO< 1 mg/l)
Slightly higher in the base case (lower panel) then in the WIP case

## Slide 10
Difference in Hypoxia volume Tangier Sound
(an aquaculture segment)
Slightly higher in the base case (lower panel) then in the WIP case

## Slide 11
Difference in Hypoxia volume Choptank Estuary
(an aquaculture segment)
High frequency variation

## Slide 12
Difference in Hypoxia volume Rappahannock Estuary
(an aquaculture segment)
Slightly higher in the base case (lower panel) then in the WIP case

## Slide 13
DO improvement across deep channel and local waters with projected oyster aquaculture in 2025 under the WIP condition
CB4.2C Bottom
CB5.2 Bottom
EE3.2 (Tangier Sound)
LE4.2 (York River)

## Slide 14
Chl changes with projected oyster aquaculture in 2025 under the WIP condition
CB4.2C Bottom
CB5.2 Bottom
EE3.2 (Tangier Sound)
LE4.2 (York River)

## Slide 15
KD improvement with projected oyster aquaculture in 2025 under the WIP condition
LE3.2 (Rappahannock)
LE1.3 (Patuxent)
LE4.2 (York River)
EE3.2 (Tangier Sound)

## Slide 16
TSS changes with projected oyster aquaculture in 2025 under the WIP condition
LE3.2 (Rappahannock)
LE1.3 (Patuxent)
EE3.2 (Tangier Sound)
LE4.2 (York River)

## Slide 17
Full oyster aquaculture buildout is estimated to improve water quality attainment in the Chesapeake locally and in deep hypoxic water.
Signal of impact on an array of water quality variables: DO, Chlorophyll, KD, and TSS.
The simulated biogeochemical nutrient reductions are about twice as effective at improving CB4MH Deep Channel DO attainment than nutrient reductions from oyster ingestion.
Summary