## Slide 1
Rosemary Fanelli, Matt Cashman, and Aaron Porter
U.S. Geological Survey
May 15, 2020
USGS/SHWG Stressor summary project update

## Slide 2: Extracting key information from selected literature
General paper information
  Author, title, journal, etc.
General study design
  Field-based study vs flume or mesocosm
  Multiple or single stressor
Methodology
  How response variable was measured (IBI, %EPT)
  How stressor(s) were quantified
Key findings
  Identified dominant stressor
  Thresholds for detectable changes in stream health
  Qualitative measures of changes in stream health
Study constraints/limitations

## Slide 3: Summarize and synthesize results
60%
17%
12%
Number of studies summarized so far = 75
Number of journals/sources covered = ~38
  Hydrobiologia (10)
  JNABS/Freshwater Science (8)
  Ecological Indicators (5)
  Freshwater Biology (5)
  STOTEN (5)
  Environmental Pollution (3)
Types of studies
  Most field, some field & modeling and lab
Provisional results, for feedback only
Notes: Predicted conditions using stressor data

## Slide 4: What types of stressors were measured?
41% examined 3 or more stressors
13% examined flow, salinity, and sediment individually
Few toxic field studies
Number of papers
Stressor
Provisional results, for feedback only

## Slide 5: Where do the stressors originate?
Out of 75 papers:
23% urbanization
17% mining
13% multiple
10% agriculture
13 papers did not have defined “source”
Number of papers
Driver/source
Provisional results, for feedback only

## Slide 6: Where do the stressors originate?
Out of 75 papers:
23% urbanization
17% mining
13% multiple
10% agriculture
13 papers did not have defined “source”
Number of papers
Driver/source
Provisional results, for feedback only

## Slide 7: Urban studies
17 studies identified urbanization as major driver
  13 studies examined multiple stressors
  1 study examined flow alteration
  3 studies examined salinity (2 of 3 had lab component)
  2 studies examined sediment
Types of urbanization
  Most leveraged rural/forest-urban gradients
  Highway construction
  Military base development
Many biological response metrics
  Abundance, total taxa richness, EPT richness, EPT-H richness, % EPT taxa, MD BIBI, Shannon diversity, FFG, evenness metrics, NMDS ordination scores, O/E ratios, etc.
Provisional results, for feedback only

## Slide 8: Urban studies- multiple stressor
Type of study: spatial urban gradient in 9 major metropolitan areas (25-30 sites in each MA)
Stressors measured: Flow alteration, temp, W/D ratios, percent fines, ions, nutrients, toxics
Bio response: observed vs expected (O/E) taxa and NMDS scores
Statistical approach for comparing stressors: single and multiple regression model comparisons
Which stressor was most important: HOCs (toxics) and hydrology
Bryant and Carlisle 2012 (Freshwater Science)
Summed AICc weights
Notes: HOC= hydrophobic organic contaminates, PAHs (polycyclic aromatic hydrocarbons)

## Slide 9: Urban studies- multiple stressor
Waite et al. 2019 (STOTEN)
Type of study: spatial urban gradient of 75 sites in SE united States
Stressors measured: Flow alteration, temp, habitat metrics, ions, nutrients, toxics
Bio response: EPTR-H richness, O/E taxa, total taxa richness
Statistical approach for comparing stressors: boosted regression trees
Which stressor was most important: hydrology, toxics (pesticides), and dissolved oxygen

## Slide 10: Agricultural studies
8 studies identified agriculture as main driver
  5 examined multiple stressors simultaneously
  2 were pesticide lab/mesocosm studies
  1 study compared 2 stressors simultaneously (sediment and velocity)
Different agricultural types and intensity
  Pasture/cattle grazing
  row crops
Wide range of biological responses
  macroinvert abundance, diversity, richness, biomass, multimetric indices of biological integrity, survival and growth, etc.
Provisional results, for feedback only

## Slide 11: Ag studies-multiple stressor
Braccia and Voshell 2006
(Hydrobiologia)
Type of study: sites spanning cattle density gradient
Stressors measured: flow, water quality (no nutrients), habitat, food sources
Biological response: Whole community, % taxa, % sensitive taxa, etc.
Statistical approach for comparing stressors: Multivariate statistical analyses (CCA), regression model comparison
Which stressor was most important: physical habitat (percent fines, substrate homogeneity)

## Slide 12
Schmidt et al. 2019 (Environmental Science and Technology)
Ag studies-multiple stressor
Type of study: 98 sites spanning row crop gradient (12 were designated urban)
Stressors measured: flow, water quality, toxics, habitat, temperature
Biological response: multi-metric index
Statistical approach for comparing stressors: structural equation modeling
Which stressor was most important: pesticides, ammonia, channel erosion (all negative effects)

## Slide 13: Next steps
Continue summarizing studies
Test out different ways to summarize data
  Sources/sectors have multiple stressors
  Stressors can originate from multiple sources
Further standardizing information collection during paper reviews
  Categorize biological responses (reference-based, richness, etc.)
Target specific literature to cover gaps (e.g., more agriculture, climate change, stream temperature studies needed)

## Slide 14: EPA ATTAINS – Impairment Analysis
What in-stream stressors and landscape causes are most important according to impairment listings?
Using most recent EPA ATTAINS data
Focus on Ecological Life Use Group
  Other groups include: Fish Consumption, Recreation, Water Supply
Impairment “parameters” grouped into larger EPA categories
  i.e. stressor groups
State-level differences obvious
Provisional results, for feedback only

## Slide 15: EPA ATTAINS – Most Frequent Parameters
Use: Ecological Life
Parameter: Not Attaining
“Cause” only
Ranked by stream miles listed in ATTAINS
Provisional results, for feedback only

## Slide 16: EPA ATTAINS – Suspected “Source”
Many state differences
Provisional results, for feedback only

## Slide 17: EPA ATTAINS – Confirmed “Source”
Many state differences
Provisional results, for feedback only

## Slide 18: EPA ATTAINS – Parameter Networks
Network analysis of co-occurring impairment parameter on same assessment unit across uses
Clusters of correlated stressors
Identifying multi-stressor groupings
Provisional results, for feedback only

## Slide 19: EPA ATTAINS – Current takeaways
In ATTAINS, the top 4 “Stressor” groupings (by mile)
  Sediment/Turbidity
  Salinity/TDS/Chlorides/Sulfates
  Nutrients
  Habitat Alterations
Network analysis of co-occurring stressor impairments identifies multi-stressor clusters related to
  Sediment/Nutrients/Habitat
  Contaminants
  Metals/Acidity
There are large state-by-state differences, in stressors, sources, and way data is stored in ATTAINS
  Work-in-progress to harmonize data
  Missing data for some listed Virginia streams
Provisional results, for feedback only